## Slide 1
Matlab Tutorial #2
Kathleen Chen
chens18@rpi.edu
February 13, 2018

## Slide 2: BB05 Fourier Series
Determination of Fourier components from the code given in the video
Use these Fourier components to create a curve close to the square wave

## Slide 3: BB06 Fourier Transform Part 2
Two answers were accepted:
  Analytical – http://www.youtube.com/watch?v=1hX_MUh8wfk
  MATLAB –

## Slide 4: Outline
Discrete Convolution
  Zero-padding
  Circular Equivalent to Linear
Spectral Analysis
  Zero-padding
  Refined Spectral Bins
2D Filtering
  Noise Removal
  Edge Enhancement

## Slide 5: Visualization of Discrete FT

## Slide 6: Hands-on Example

## Slide 7: Multiplications at n=0
0
1
2
3
4
f(k)
0
-4
2
3
4
g(-k)
-3
-2
-1
1

## Slide 8: Multiplications at n=8
0
1
2
3
4
f(k)
0
-4
2
3
4
g(8-k)
-3
-2
-1
1

## Slide 9: Functional example
h(n)
X(n)
Linear convolution result of X(n) and h(n)
XN(n) where X is now periodic with N components (“circularly extended”)
Components of linear convolution of XN(n), h(n)
  Edge effects
Composite output (green section is unaffected by edge effects (“desired” solution)
*We would need zero padding here!*

## Slide 10: Hands-on Result
>>
x=[5 4 3 2 1];
h=[1 2 3 4 5];
y=conv(x,h);
plot(y); ylim([0 100]);
>>

## Slide 11: Circular Convolution

## Slide 12: Convolution with Zero Padding

## Slide 14
Circular convolution w/o zero padding ≠ Linear convolution!

## Slide 16: Outline
Discrete Convolution
  Zero-padding
  Circular Equivalent to Linear
Spectral Analysis
  Zero-padding
  Refined Spectral Bins
2D Filtering
  Noise Removal
  Edge Enhancement

## Slide 17: Synthetic Waveform
Fs = 1e3;
t = 0:0.001:1‐0.001;
x = cos(2*pi*100*t)+sin(2*pi*202.5*t);
Plot(x(1:100));
https://www.mathworks.com/help/signal/ug/amplitude-estimation-and-zero-padding.html

## Slide 18: Without Zero Padding
xdft = fft(x);
xdft = xdft(1:length(x)/2+1);
xdft = xdft/length(x);
xdft(2:500) = 2*xdft(2:500);
freq = 0:Fs/length(x):Fs/2;
plot(freq,abs(xdft))
hold on
plot(freq,ones(length(x)/2+1,1),'LineWidth',2)
xlabel('Hz')
ylabel('Amplitude')
hold off
The 202.5 frequency is not well-resolved Not within the default spectral bins (1 Hz)

## Slide 19: With Zero Padding
xdft = fft(x,2000);
xdft = xdft(1:length(xdft)/2+1);
xdft = xdft/length(x);
xdft(2:500) = 2*xdft(2:500);
freq =0:Fs/(2*length(x)):Fs/2;
plot(freq,abs(xdft))
hold on
plot(freq,ones(2*length(x)/2+1,1),'LineWidth',2)
xlabel('Hz')
ylabel('Amplitude')
hold off
Both frequencies are well-resolved Within the default spectral bins (spacing between DFT bins is Fs/2000 = 0.5Hz)

## Slide 20
Continuous Function

## Slide 21
The 202.5, 445.8 frequencies are not well-resolved; Frequencies are not discrete

## Slide 22
The 445.8 frequencies is not well-resolved; Frequencies are not discrete

## Slide 23
All frequencies are well-resolved!

## Slide 24: Outline
Discrete Convolution
  Zero-padding
  Circular Equivalent to Linear
Spectral Analysis
  Zero-padding
  Refined Spectral Bins
2D Filtering
  Noise Removal
  Edge Enhancement

## Slide 25: 2D Fourier Transform

## Slide 26: Noise Suppression
FT
IFT

## Slide 27: Low-/High-pass Filtering

## Slide 28: 2D Image Filters

## Slide 29: Filtered Images

## Slide 30
ArtX Homework: Overview Poster
Shift-invariant Linear System
Convolution
Fourier Series
Fourier Transform
Signal Processing
DFT & FFT
Periodic
Non-periodic
Function/System
Due Fri