## Slide 1
38655 BMED-2300-02
Lecture 10: Network
Ge Wang, PhD
Biomedical Imaging Center
CBIS/BME, RPI
wangg6@rpi.edu
February 16, 2018

## Slide 2
Tue | Topic | Fri | Topic
1/16 | Introduction | 1/19 | MatLab I (Basics)
1/23 | System | 1/26 | Convolution
1/30 | Fourier Series | 2/02 | Fourier Transform
2/06 | Signal Processing | 2/09 | Discrete FT & FFT
2/13 | MatLab II (Homework) | 2/16 | Network
2/20 | No Class | 2/23 | Exam I
2/27 | Quality & Performance | 3/02 | X-ray & Radiography
3/06 | CT Reconstruction | 3/09 | CT Scanner
3/20 | MatLab III (CT) | 3/23 | Nuclear Physics
3/27 | PET & SPECT | 3/30 | MRI I
4/03 | Exam II | 4/06 | MRI II
4/10 | MRI III | 4/13 | Ultrasound I
4/17 | Ultrasound II | 4/20 | Optical Imaging
4/24 | Machine Learning | 4/27 | Exam III
BB Schedule for S18
Office Hour: Ge Tue & Fri 3-4 @ CBIS 3209 | wangg6@rpi.edu
Kathleen Mon 4-5 & Thurs 4-5 @ JEC 7045 | chens18@rpi.edu

## Slide 3: Closely Related Concepts
Function
System
Network

## Slide 4
V-I Relationship for Resistor

## Slide 5
V-I Relationship for Capacitor

## Slide 6
V-I Relationship for Inductor

## Slide 7: Phasor
Phasor Notation
Stable Response of an RCL Circuit to a Sinusoidal Excitation Remains Sinusoidal at the Same Frequency

## Slide 8: Imaginary i Revisited

## Slide 9: V-I Relationship for Capacitor

## Slide 10: V-I Relationship for Inductor

## Slide 11
Impedance
Resistance in a Generalized Form:
Z=V/I

## Slide 12: Electrical Network
+
-
Vs
Is
R1
R2
R3
+
Vo
-
Node – Point where circuit elements are connected
Branch – Circuit element between two nodes
Loop – Closed path through any node/branch only once

## Slide 13: How Many Nodes?
+
-
Vs
Is
R1
R2
R3
+
Vo
-

## Slide 14: How Many Loops
+
-
Vs
Is
R1
R2
R3
+
Vo
-

## Slide 15: Kirchhoff’s Current Law (KCL)
The sum of the currents into & out of a node equals zero
I1=2A
I2=3A
I3=5A

## Slide 16: Kirchhoff’s Voltage Law (KVL)
The sum of the potential differences around a closed loop equals zero
V1=10V
V5=1V
V3=3V
V2=2V
V6=4V
V4=0V

## Slide 17: Adding Loops and/or Nodes
KCL + KVL = Unique Solution

## Slide 18: Example
KCL for Node c
KVL for Loop befcb
KVL for Loop abcda

## Slide 19: Ohm’s Law Revisited
Ohm’s Law generalized for an AC circuit –
V=ZI (vs V=RI)
  Resistor: V & I in phase
  Capacitor: V lags I by 90o
  Inductor: V leads I by 90o
Component |  | Impedance | 
Resistor | ZR |  | 
Capacitor | ZC |  | 
Inductor | ZL |  | 

## Slide 20: Equivalent Impedance (Prove!)

## Slide 21: Analog Low-Pass Filter

## Slide 22: More Filters

## Slide 23: AC is DC in Disguise

## Slide 24: Voltage Divider: Signal Transfer
Needs
Large Input Resistance
Small Output Resistance
Great Magnification/Gain
Sensitivity Analysis
  Interested in measuring any change x of the sensor: RS=R0(1+x)
  R0 is the nominal sensor resistance
  Load resistor expressed as RL=R0k

## Slide 25: Wheatstone Bridge
Combination of Two Dividers
  Reference divider
  Sensor divider
Operating Modes
  Null mode
  Deflection mode
R1
Needs
Large Magnification/Gain

## Slide 26: Nonlinear Components

## Slide 27: Op Amp Model
Op Amp Consists of Many Transistors
But can be Simply Modeled

## Slide 28: Operational Amplifier
Parameter | Ideal | Typical
Open-loop voltage gain A | ∞ | 105 – 109
Common mode voltage gain | 0 | 10-5
Frequency response f | ∞ | 1- 20 MHz
Input impedance Zin | ∞ | 106 Ω (bipolar), 109–1012 Ω (FET)
Output impedance Zout | 0 | 100 – 1000 Ω

## Slide 29: Two Rules

## Slide 30: Example

## Slide 31: Common Modules
http://www.rfcafe.com/references/electrical/opamps.htm

## Slide 32: Measuring Instruments

## Slide 33: AAAS Meeting

## Slide 34: AI Talk at AAAS (Feb. 2016)

## Slide 35: New Revolution
Industrial Revolution
Information Revolution
Intelligence Revolution

## Slide 36: Scientific Philosophy

## Slide 37: Biological Neuron
Axons carry information from the cell body to the axon terminals
Axon terminals communicate with their target cells at synapses
https://upload.wikimedia.org/wikipedia/commons/a/a9/Complete_neuron_cell_diagram_en.svg

## Slide 38: Simpler Version
https://www.tutorialspoint.com/artificial_intelligence/artificial_intelligence_neural_networks.htm

## Slide 39: Simplest Version
Body (Soma)
Fiber (Axon)
Branches (Dendrite)
Weight
Transformation (Nonlinear)
Summation (Linear)
Biological Neuron
Artificial Neuron
Input
Input
Output
Output
Interface (Synapsis)

## Slide 40: Perceptron

## Slide 41: Artificial Neural Network
https://www.extremetech.com/extreme/215170-artificial-neural-networks-are-changing-the-world-what-are-they

## Slide 42
http://www.asimovinstitute.org/neural-network-zoo/

## Slide 43: Not All Configurations Useful
Key Insights
Multi-scale Analysis (Wavelet Transform)
Convolutional Operation (Linear System)
Shortcut/Feedback (Control Theory)
Adversarial Mechanism (Game Theory)
Amplitude/Phase (Complex Analysis)
… …

## Slide 44: Gradient Descent Search

## Slide 45: MATLAB ML Toolbox

## Slide 46: Gradient Direction
Additional Links:
How to Do Gradient Search?
https://medium.com/ai-society/hello-gradient-descent-ef74434bdfa5
How to Train Neural Network?
http://blog.manfredas.com/backpropagation-tutorial/#more-848

## Slide 47: Key Idea for Back Propagation
http://blog.manfredas.com/backpropagation-tutorial/#more-848

## Slide 48: IEEE Perspective
http://ieeexplore.ieee.org/document/7733110/

## Slide 49: Improving Signal-to-Noise Ratio
https://micro.magnet.fsu.edu/primer/digitalimaging/concepts/ccdsnr.html

## Slide 50: Ge’s Poster

## Slide 51: Copyright Issue

## Slide 52
BB10 Homework
Find Vout in terms of Vcc and resistances
Find the sensitivity of this circuit dVout/dx
Find RL do to maximize the sensitivity
Due Date: Same (Week Later)
Sensitivity Analysis
  Interested in measuring any change x of the sensor: RS=R0(1+x)
  R0 is the nominal sensor resistance
  Load resistor expressed as RL=R0k
Optional Reading:
http://ieeexplore.ieee.org/document/7733110/