## Slide 1
38655 BMED-2300-02
Lecture 16: Nuclear Physics
Ge Wang, PhD
Biomedical Imaging Center
CBIS/BME, RPI
wangg6@rpi.edu
March 23, 2018

## Slide 2
Tue | Topic | Fri | Topic
1/16 | Introduction | 1/19 | MatLab I (Basics)
1/23 | System | 1/26 | Convolution
1/30 | Fourier Series | 2/02 | Fourier Transform
2/06 | Signal Processing | 2/09 | Discrete FT & FFT
2/13 | MatLab II (Homework) | 2/16 | Network
2/20 | No Class | 2/23 | Exam I
2/27 | Quality & Performance | 3/02 | X-ray & Radiography
3/06 | CT Reconstruction | 3/09 | CT Scanner
3/20 | MatLab III (CT) | 3/23 | Nuclear Physics
3/27 | PET & SPECT | 3/30 | MRI I
4/03 | Exam II | 4/06 | MRI II
4/10 | MRI III | 4/13 | Ultrasound I
4/17 | Ultrasound II | 4/20 | Optical Imaging
4/24 | Machine Learning | 4/27 | Exam III
BB Schedule for S18
Office Hour: Ge Tue & Fri 3-4 @ CBIS 3209 | wangg6@rpi.edu
Kathleen Mon 4-5 & Thurs 4-5 @ JEC 7045 | chens18@rpi.edu

## Slide 3: Nuclear Physics
General Perspective
Radioactivity
Decay Mechanisms
Decay Modeling
Tracer Production
Devices
Milking Modeling
Data Acquisition
Gamma Camera
Coincidence Detection

## Slide 4: Marie Curie

## Slide 5: Michael Ter-Pogossian
Michel Matthew Ter-Pogossian (April 21, 1925 – June 19, 1996) was one of the fathers of positron emission tomography (PET), the first functional brain imaging technology. PET can evaluate the brain during mental processes versus looking at the structure through conventional CT.

## Slide 6: X-ray CT
Water
Air
Fat
50%
Calcium 150mg/ml
Iodine
20mg/ml
Gold
10mg/ml
X-ray Tube
Rotation
Photon-integrating
Detector
Photon-counting
Detector
Averaged
Linear Attenuation
Over Whole X-ray Spectrum
Conventional CT
Spectral Molecular CT
Full Spectrum
For K-edges
In Many Energy Bins
Multi-material Phantom
600
0

## Slide 7: Basic Idea of Nuclear Imaging

## Slide 8: Further Illustrated

## Slide 9: Physical Principles
Unstable Isotope as Tracer Molecule (Radionuclide)
Administered Intravenously or Orally
Metabolic Process Involved
Gamma Rays Emitted
Measurement of Metabolism/Function

## Slide 10: Similarities & Differences
Similarities
Similar Energy Levels
Straight Ray Geometries
Line Integrals
Tomographic Recons
Differences
External vs Internal Sources
Anatomical vs Functional
High vs Low Flux/Resolution
Low vs High Sensitivity

## Slide 11: PET-CT
Major Strength of Nuclear Imaging:
Label Most Metabolites
Highly Sensitive Biochemically
In the Best Form of the Hybrid Scanner,
Such as PET-CT & PET-MRI

## Slide 12: Nuclear Physics
General Perspective
Radioactivity
Decay Mechanisms
Decay Modeling
Tracer Production
Devices
Milking Modeling
Data Acquisition
Gamma Camera
Coincidence Detection

## Slide 13: Atomic Number & Mass Number
Atomic Number (Z): the number of protons in its nucleus
Atomic Weight (≃A): In most cases the mass number, equal to the total number of protons and neutrons

## Slide 14: Isotopes
Isotopes of a Chemical Element Have the Same Atomic Number but Different Mass Numbers (Different Numbers of Neutrons)
Examples: 12Carbon and 14C
Isotopes May Emit Radiation

## Slide 15: Gamma Rays
Unstable Nucleus Changes from a Higher to Lower Energy State through Gamma Ray Emission
Gamma Rays Have Similar Energies as X-rays but Are Generated Differently:
X-ray through Electron Interaction
Gamma-ray through Isometric Transition

## Slide 16: Decay Types
Alpha (α)
Beta (β- & β+)
Gamma ()
Electron Capture

## Slide 17: Alpha Decay
Alpha-particle Decay/Nucleon Emission
Heavy Damage to Tissue
Example: α-photon of 3-7 MeV

## Slide 18: Beta Decay

## Slide 19: Positron Emission

## Slide 20: Gamma Decay
Immediate Release of a -photon
Metastable State for
Delayed Release of
a –photon (& an Antineutrino)

## Slide 21: Gamma Decay: 99mTc

## Slide 22: Electron Capture
Change a Proton to a Neutron
Excited Nucleus
+ X-rays or Auger Electrons
+ Inner Bremsstrahlung

## Slide 23: Another Classification
https://www.slideshare.net/KenCzerwinski/chem-312-lect-1-2013-intro-show

## Slide 24: Common Tracers

## Slide 25: Exponential Decay

## Slide 26: Mathematical Details

## Slide 27: Nuclear Physics
General Perspective
Radioactivity
Decay Mechanisms
Decay Modeling
Tracer Production
Devices
Milking Modeling
Data Acquisition
Gamma Camera
Coincidence Detection

## Slide 28: Four Methods

## Slide 29: Nuclear Reactor (1st & 2nd Methods)
Neutron Capture & Nuclear Fission

## Slide 30: Nuclear Fission (2nd Method)
In nuclear physics, nuclear fission is either a nuclear reaction or a radioactive decay process in which the nucleus of an atom splits into lighter nuclei. The fission process often produces free neutrons and gamma photons, and releases a huge amount of energy.

## Slide 31: Cyclotron (3rd Method)

## Slide 32: Cyclotron Example

## Slide 33: Generator (4th Method)

## Slide 34: Two-step Process

## Slide 35: Dynamic Modeling

## Slide 36: Daily Yield
The ratio of the two species is constant – the decay rate of the daughter is governed by the half-life of the parent.

## Slide 37: Clinical Applications

## Slide 38: Nuclear Physics
General Perspective
Radioactivity
Decay Mechanisms
Decay Modeling
Tracer Production
Devices
Milking Modeling
Data Acquisition
Gamma Camera
Coincidence Detection

## Slide 39: Gamma Camera

## Slide 40: Collimator

## Slide 42: Polycapillary Lens of Gamma Rays?

## Slide 43: Crystal

## Slide 44: Signal Detection: PMT

## Slide 45: Signal Localization: Anger Network

## Slide 46
Threshold the Signal
Localize the Signal
Light to Electric Signal
Gamma Photon to Light
Collimate Gamma Rays
Synchronize the Signal
Planar Scintigraphy

## Slide 47: Energy Spectra

## Slide 48: Spatial Resolution

## Slide 49: Point Spread Function

## Slide 50: Dead Time

## Slide 51: FDG for Cancer Imaging
Positron emission tomography (PET) is a functional imaging technique that is used to observe metabolic processes in the body. If the biologically active molecule chosen for PET is fludeoxyglucose (FDG, produced in Cyclotron), an analogue of glucose, the concentrations of tracer imaged will indicate tissue metabolic activity as it corresponds to the regional glucose uptake. Use of this tracer to explore the possibility of cancer metastasis (i.e., spreading to other sites) is the most common type of PET scan (90% of current scans).

## Slide 52: Coincidence Detection
  Pulses from PMT Go through the Coincidence Circuit to Check if the Signals are from the Same Event
  Signals Go through the Energy Window to Reject Scatters
Pulse Height Analyzer

## Slide 53: Coincidence: Paired Pulses

## Slide 54: Time of Flight Detection

## Slide 55
BB16 Homework
Due Date: Same (1 Working Week Later)