## Slide 1
Midterm Review (Not Exclusive)
Ge Wang
AI-based X-ray Imaging System (AXIS) Lab
Rensselaer Polytechnic Institute, Troy, New York, USA
October 26, 2020

## Slide 2: MI Schedule for F20
Tue | Topic | Fri | Topic
09/01 | Introduction | 09/04 | Neuron, Network & Backpropagation
09/08 | No Class | 09/11 | Hands-on 1: Python, Colab, & TensorF
09/15 | Architectures | 09/18 | Minds-on & Hands-on 2: MNIST Classification
09/22 | Image Quality I | 09/25 | CT Physics
09/29 | CT Reconstruction | 10/02 | Deep CT Reconstruction
10/06 | Hands-on 3: CT Networks | 10/09 | More CT Contents
10/13 | MRI Physics | 10/16 | Spin-Echo
10/20 | K-Space Theorem | 10/23 | More MRI Contents
10/26 | Midterm Review; 10/27 Mid Exam | 10/30 | Deep MRI Reconstruction
11/03 | Hands-on 4: MRI Networks | 11/06 | Nuclear Physics
11/10 | Nuclear Imaging | 11/13 | US Imaging
11/17 | Optical Imaging | 11/20 | Multimodality Imaging
11/24 | Hands-on 5: Image Conversion | 11/27 | Thanksgiving
12/01 | Image Quality II | 12/04 | Stability, Interpretability, & Others
12/08 | Overview | 12/11 | Final Exam

## Slide 3: DOT URL: http://161.35.62.103.80/
F20MI-Midterm-DOT

## Slide 4: Notes

## Slide 5: Survey Results in the Last Semester

## Slide 7: Midterm Distribution in Fall, 2018
A+
A
B
B+
B-
C

## Slide 9: Outline
MRI
CT
NN

## Slide 10: Signal Model with Gradients
Spin-Echo Signal Model for a Whole Object with a 90˚ Pulse in the Rotating Frame
Signal Model with Gradient Fields
Signal Model for a Whole Object in the lab frame
Voxel-specific accumulated phase factor
Relative to ω0
A trajectory point in the k-space after the volumetric integral at time instant t
Voxel-specific angular frequency in the inner product format

## Slide 11: K-Theorem as the Foundation of MRI
This is the standard spin-echo signal model in the rotating frame for a whole object
This defines a “k” point as a function of time in the k-space, still in the rotating frame. Each k point is computed by integrating over the whole object space (the nature of FT)
We need to let the “k” point trace the whole Fourier spectral support so that the inverse Fourier transform can be used to reconstruct the original image
The Fourier imaging model is again approximate, just like in the CT case

## Slide 12: 2D Spin-Echo
t=TE/2
t=0
t=TE
Rephasing
Slice Selection Spin-Echo Reading
Ladder
=
=
Dephasing from midpoint (Eq. (4.42) in BB

## Slide 14: Bloch Eqs. in the Rotating Frame

## Slide 15: Spectroscopy Method: PRESS
  (Point Resolved Spectroscopy)

## Slide 16: MRI System Diagram
https://nationalmaglab.org/education/magnet-academy/learn-the-basics/stories/mri-a-guided-tour

## Slide 17: Gradient Coils
Longitudinal Gradient
Transverse Gradient

## Slide 18: Outline
MRI
CT
NN

## Slide 20: Derivation of Beer’s Law

## Slide 21: Sinusoidal Waves Are Building Blocks

## Slide 22: Probing Waves
No any info in projection data along non-orthogonal directions
Info in projection data along the orthogonal direction

## Slide 23: 1D Fourier Slice
2D Fourier Transform
1D Fourier Transform
X-rays
Radon Transform

## Slide 24: Fourier Slice Theorem

## Slide 26: Parallel- to Fan-beam FBP
Parallel-beam
Filtered Backprojection
Fan-beam
Filtered Backprojection
Key Idea: Convert Fan-beam Data to Parallel-beam Data or We Do It Heuristically!

## Slide 27: Backprojection from One Angle
Projection
r
r
r
r
r

## Slide 28: Cone-beam Scanning
β
α
General Scanning Trajectory

## Slide 29: Obliqueness Correction
Obliqueness Correction in Fan-beam Formula
Obliqueness Correction in Cone-beam Formula
An X-ray Hits the 2D Detector Plate Obliquely, Determined by Two Angles

## Slide 30: Data Acquisition System (DAS)
Filter
Source
Detector
Pre-Collimator
Post-Collimator
Patient
Scattering

## Slide 31: CT Scanning Modes

## Slide 32: Outline
MRI
CT
NN

## Slide 33: Biological & Artificial Neurons
Body (Soma)
Fiber (Axon)
Branches (Dendrite)
Weight
Transformation (Nonlinear)
Summation (Linear)
Biological Neuron
Artificial Neuron
Input
Input
Output
Output
Interface (Synapsis)

## Slide 34: Programming vs Data-driven Learning
Data
Output
Training
Data
Program
Output
Data
Output
Program

## Slide 35: Backpropagation Algorithm (Book)
(3.17)

## Slide 36: Single Layer Operation

## Slide 37: Feed Forward 1-layer Network for 10 Classes
https://cloud.google.com/blog/products/gcp/learn-tensorflow-and-deep-learning-without-a-phd

## Slide 38: Derivation of Softmax Function
http://willwolf.io/2017/04/19/deriving-the-softmax-from-first-principles/
These pseudo likelihood values are in a relative sense! –
We can set one as ground 0
These pseudo likelihood values are again in a relative sense!
Note -5, 7, -2 will make the denominator 0
Make sure non-negative
We can normalize these likelihood values to produce probabilities.

## Slide 39
http://www.asimovinstitute.org/neural-network-zoo/

## Slide 40: Convolutional Layer
https://stats.stackexchange.com/questions/142606/receptive-field-of-neurons-in-lenet

## Slide 41: Recognizing Your Digits
Read an image file
Normalize it
Resize to
a desired size
Pass into the network

## Slide 42: Auto-encoder
This is one of the greatest ideas in deep learning. If you explore more, you can create more advanced networks!

## Slide 43: U-Net for Denoising & More

## Slide 44: AUTOMAP with Complexity
Zhu B, Liu JZ, Cauley SF, Rosen BR, Rosen MS: Image reconstruction by domain-transform manifold learning. Nature 555:487–492, 2018
k-space Data
Reshape
To a Vector
FC Layers to All Pixels
Image
Complexity
# of Data or Pixels per Row
# of views
Notes: In the literature, only a few deep-learning methods were proposed for reconstructing medical images directly from raw data. AUTOMAP, published last year on Nature, is the first work trying to learn the reconstruction process. N denotes the dimension of reconstructed image. AUTOMAP use 3 fully-connected layers to the the mapping between raw k-space data to a corresponding MRI images. The basic idea of AUTOMAP could be illustrated here. Due to the intrinsic relation between frequency domain and time domain, every pixel in k-space domain is related every pixel in image domain. Fully-connected layer is able to learn this relation. Without a doubt, similar idea could be applied to CT since sinograms and images are also correlated. If we directly apply AUTOMAP for CT applications, the complexity would be . N_v donotes the number of view. There are two problems if we use AUTOMAP for CT: 1. Due to the large computational complexity, AUTOMAP is not able to train normal size CT images on modern GPUs. In the AUTOMAP paper, authors used 128*128 images. 2. FC layers imply that all the pixels in both domain are correlated, but this is not the true for CT. In CT imaging, x-ray are used to take line integral at various angle, so a single point in the sinogram only relate to a line in the field of view.
In the literature, only a few deep-learning methods were proposed for reconstructing medical images directly from raw data. AUTOMAP, published last year on Nature, is the first work trying to learn the reconstruction process. N denotes the dimension of reconstructed image. AUTOMAP use 3 fully-connected layers to the the mapping between raw k-space data to a corresponding MRI images. The basic idea of AUTOMAP could be illustrated here. Due to the intrinsic relation between frequency domain and time domain, every pixel in k-space domain is related every pixel in image domain. Fully-connected layer is able to learn this relation. Without a doubt, similar idea could be applied to CT since sinograms and images are also correlated. If we directly apply AUTOMAP for CT applications, the complexity would be 𝑶(𝑵^𝟑×𝑵_𝒗 ). N_v donotes the number of view. There are two problems if we use AUTOMAP for CT: 1. Due to the large computational complexity, AUTOMAP is not able to train normal size CT images on modern GPUs. In the AUTOMAP paper, authors used 128*128 images. 2. FC layers imply that all the pixels in both domain are correlated, but this is not the true for CT. In CT imaging, x-ray are used to take line integral at various angle, so a single point in the sinogram only relate to a line in the field of view.

## Slide 45: iCTNet with Complexity
*Li, Y., Li, K., Zhang, C., Montoya, J. and Chen, G., “Learning to Reconstruct Computed Tomography (CT) Images Directly from Sinogram Data under A Variety of Data Acquisition Conditions,” IEEE Transactions on Medical Imaging, 1–1 (2019).
sinogram
sinogram
FC
FC
image
image
final output
Notes: The second work trying to learn the reconstruction process is the iCTNet published on IEEE transaction on medical imaging this year. N_c denotes the number of detectors. The overall idea of iCTNet can be summarized here. Assume a CT scanner with 3 detectors and 4-view sinogram is acquired. iCTNet contains a total of 12 layers, in the first 8 layers, convolutional layers are used to de-noised sinogram, and to learn the interpolation process, generating a learned full-view sinogram with number of view , where is a hyperparameter in iCTNet. Then, instead of feeding the whole sinogram into one large FC layer, iCTNet feeds projection at each angle in to a small FC layer, thereby reducing the computation burden. Rotation operations are used to synthesis the analytical FBP method and then one convolutional layer is used to combine all the images at different angle, generating final output.
The second work trying to learn the reconstruction process is the iCTNet published on IEEE transaction on medical imaging this year. N_c denotes the number of detectors. The overall idea of iCTNet can be summarized here. Assume a CT scanner with 3 detectors and 4-view sinogram is acquired. iCTNet contains a total of 12 layers, in the first 8 layers, convolutional layers are used to de-noised sinogram, and to learn the interpolation process, generating a learned full-view sinogram with number of view 4𝛼, where 𝛼 is a hyperparameter in iCTNet. Then, instead of feeding the whole sinogram into one large FC layer, iCTNet feeds projection at each angle in to a small FC layer, thereby reducing the computation burden. Rotation operations are used to synthesis the analytical FBP method and then one convolutional layer is used to combine all the images at different angle, generating final output.

## Slide 46: Our Key Idea: Smart BP with Complexity
Smart Backpropagation with Learned Weights Restricted to a Single X-ray Path
Learned Filtered Projection

## Slide 47: Adversarial Learning
Data
Frequency
1.0
0.5
Data/
Target/Real Distribution
Synthetic/
Source/Fake Distribution